## Slide 1
STEROWNIK POWER-TO-HEAT · SHELLY
Sterowanie grzałkami z nadwyżki PV
+ pompa obiegowa
Nadwyżka fotowoltaiki grzeje bufor i CWU — w całości na Shelly, bez chmury i Home Assistanta.
Układ power-to-heat na Shelly: nadwyżka fotowoltaiki grzeje bufor przez stopnie grzałek, a pompa obiegowa przepompowuje ciepło do zasobników CWU. Całość steruje jeden skrypt na Shelly 1PM Gen4.
FUNKCJE
Grzanie z nadwyżki PV
Stopnie 2 kW dokładane dynamicznie z eksportu mierzonego przez Pro 3EM — nigdy nie pobiera z sieci.
Różnicówka pompy
Ciepło bufor→CWU z histerezą 10/6 °C i limitem anty-oparzeniowym.
W pełni lokalnie
Skrypt na urządzeniu — bez scen w chmurze, bez Modbusa, bez Home Assistanta.
Warstwy bezpieczeństwa
Limit bufora, watchdog grzałek, fail-safe pomiaru, filtr błędu 85 °C.
Elastyczna konfiguracja
Rozmieszczenie czujników w jednym bloku — podział między urządzenia zmienia flaga.
ARCHITEKTURA
Pro 3EM
nadwyżka
Moduł
CWU 2/3
Bufor + CWU 1
lokalnie
MASTER · 1PM Gen4
skrypt / logika
Pompa
lokalnie
3× Pro 3
grzałki
ZESTAW
2× Shelly 1PM Gen4 + Add-on master + moduł pomiarowy
Shelly Pro 3EM pomiar nadwyżki (3× CT)
3× Shelly Pro 3 grzałki — 9× 2 kW
4× DS18B20 bufor + 3× CWU
Sterownik power-to-heat na Shelly · dokumentacja i skrypt: repozytorium GitHub

## Slide 2
POWER-TO-HEAT CONTROLLER · SHELLY
PV-surplus heater control
+ circulation pump
Surplus solar heats the buffer and DHW — entirely on Shelly, no cloud, no Home Assistant.
A Shelly power-to-heat system: PV surplus heats a buffer via staged electric heaters, and a circulation pump moves heat into DHW cylinders. One script on a Shelly 1PM Gen4 runs it all.
FEATURES
PV-surplus heating
2 kW stages added dynamically from export measured by the Pro 3EM — never imports.
Differential pump
Moves heat buffer→DHW with 10/6 °C hysteresis and an anti-scald limit.
Fully local
On-device script — no cloud scenes, no Modbus, no Home Assistant.
Safety layers
Buffer cutoff, heater watchdog, measurement fail-safe, 85 °C sensor-error filter.
Flexible configuration
Sensor placement in a single block — rebalance across devices with a flag.
ARCHITECTURE
Pro 3EM
surplus
Module
DHW 2/3
Buffer + DHW 1
local
MASTER · 1PM Gen4
script / logic
Pump
local
3× Pro 3
heaters
HARDWARE
2× Shelly 1PM Gen4 + Add-on master + measurement module
Shelly Pro 3EM surplus metering (3× CT)
3× Shelly Pro 3 heaters — 9× 2 kW
4× DS18B20 buffer + 3× DHW
Shelly power-to-heat controller · docs & script: GitHub repository